## Slide 1: Signed 2’s Complement Number
Signed numbers are represented as 2’s complement numbers in computers
Recognize a signed 2’s complement number
  Sign bit = 0, positive number, recognize as a regular binary number
    0101 = +5;
  Sign bit = 1, negative number, the magnitude of the number is obtained by 2’s complement operation
    1011
      Sign: negative number
      Magnitude: 2’s complete operation of (1011) = 0100+1 = 0101 = 5
      So 1011 = 5

## Slide 2: Ranges of Signed 2’s Complement Number
In general the 2’s complement values range from 2n-1 to 2n-1-1
For n = 4, the 2’s complement values range from 8 to 7
For n = 8, the 2’s complement values range from 128 to 127
For n = 16, the 2’s complement values range from 215 to 215-1
Overflow
  If an n-bit 2’s complement number is greater than 2n-1-1 or less than 2n-1, we say there is an overflow

## Slide 3: Detecting Overflow: Method 1
Overflow detection logic
  Two numbers’ sign bits are the same but are different from the result’s sign bit
  If the two numbers’ sign bits are different, overflow is impossible
    Adding a positive and negative can’t exceed largest magnitude positive or negative
4-bit example
0
1
1
1
1
0
0
0
+
0
0
0
1
sign bits
overflow
(
a
)
1
1
1
1
0
1
1
1
+
0
1
0
0
overflow
(
b
)
1
0
0
0
1
1
1
1
+
1
0
1
1
no overflow
(
c
)

## Slide 4: Detecting Overflow: Method 2
Simpler method: Detect difference between carry-in to sign bit and carry-out from sign bit
overflow = c4  c3
0
1
1
1
1
1
1
1
0
0
1
0
0
0
+
0
0
0
1
overflow
(
a
)
1
1
1
0
0
0
1
0
1
1
1
+
0
1
0
0
overflow
(
b
)
1
0
0
0
0
0
0
1
1
1
1
+
1
0
1
1
no overflow
(
c
)
If the carry into the sign bit column differs from the
carry out of that column, overflow has occurred.

## Slide 5: CMOS Transistor
CMOS – Complementary Metal-Oxide-Semiconductor
Transistors with CMOS technology
does not
conduct
0
conducts
1
gate
nMOS
does not
conduct
1
gate
pMOS
conducts
0
Silicon -- not quite a conductor or insulator: Semiconductor

## Slide 6: AND Logic
Definition of AND operation
Z = X • Y means Z = 1 if and only if both X = 1 and Y = 1;
X | Y | Z = XY
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input AND gate
0
1
x
y
Z
y
x
AND operator
Variable

## Slide 7: OR Logic
Definition of OR operation
Z = X + Y means Z = 1 if either X=1 or Y=1, or both;
X | Y | Z = X + Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table
2-input OR gate
0
1
y
x
x
y
Z
OR operator

## Slide 8: NOT Logic
Definition of NOT operation
Z = X’ or Z = X means Z = 0 if X = 1; Z = 1 if X = 0; Z is the complement of X
X | Z = X’
0 | 1
1 | 0
Truth Table
NOT gate/Inverter
1
0
Z
x
NOT operator

## Slide 9: More Gates
NAND: Opposite of AND (“NOT AND”)
NOR: Opposite of OR (“NOT OR”)
XOR: outputs 1 when inputs have odd number of 1’s
XNOR: Opposite of XOR (“NOT XOR”)
x
0
0
1
1
y
0
1
0
1
F
1
0
0
1
x
0
0
1
1
y
0
1
0
1
F
0
1
1
0
x
0
0
1
1
y
0
1
0
1
F
1
0
0
0
x
0
0
1
1
y
0
1
0
1
F
1
1
1
0
x
y
x
y
F
F
NOR
NAND
XOR
XNOR
1
0
x
y
F
x
y
1
0
x
x
y
y
F
NAND
NOR
AND in CMOS: NAND with NOT
OR in CMOS: NOR with NOT
So NAND/NOR more common